## Slide 1
Neural Interfaces and Bionic Limbs Spring 2024
Linear Discriminant Analysis (LDA): EMG Pattern Recognition & Classification
Timothy Young, Erin Radcliffe, Sari Younan, Fai Au
GitHub Project Repo:https://github.com/sayounan/RoboArms

## Slide 2
Program Architecture – UML diagram
Input Data Structure
Data Processing
Filter Design
Off section removal
Quiescent data removal
Feature Extraction: MAV, SSC, ZC, WL
Bin sizes
Output Data Structure
Mean and SD calculations/subcalculations
Sb, Sw, O matrices
Eigenvector and Eigenvalue computations
W matrix
LDA Classification
LDA Confusion Matrix

## Slide 3
Raw Data Structure and Properties
% each mat file is a 1x1 struct (named posture) with 4 fields:
% Channels (8x25 char), Fs (2.222222167968750e+03),
% Time (8x167761 double), Data (8x167761 double)
posture_names = {'HC', 'HO', 'off', 'RD', 'Tab', 'Tad', 'UD', 'WE', 'WF', 'WP', 'WS'};
n_postures = 11;
% emg_train_struct: 1x1 struct with 11 fields, each field (posture.Data) is a 8x167761 double
% emg_val_struct: 1x1 struct with 11 fields, each field (posture.Data) is a 8x167761 double
% Example Plot of all channels of Raw EMG per posture
Notes: %% MatLab directory organization
clear all; close all; clc;
main_dir = 'C:\MATLAB\GitHub\EMG_LDA';
raw_data_dir = 'C:\MATLAB\GitHub\EMG_LDA\Group1_2024_quatro_sensors'; % Group 1 EMG
filt_data_dir = 'C:\MATLAB\GitHub\EMG_LDA\Filtered_Group1_2024_quatro_sensors'; % Filtered Group 1 EMG
cd(raw_data_dir)
%% Data exploration: load Raw EMG (Group 1) and save training and validation posture data into separate structs
mat_files = dir('*.mat');
% each mat file is a 1x1 struct (named posture) with 4 fields:
% Channels (8x25 char), Fs (2.222222167968750e+03),
% Time (8x167761 double), Data (8x167761 double)
posture_names = {'HC', 'HO', 'off', 'RD', 'Tab', 'Tad', 'UD', 'WE', 'WF', 'WP', 'WS'};
n_postures = 11;
% Raw EMG training posture data
for i = 1:n_postures
load([posture_names{1,i},'_train.mat'])
emg_train_struct.(posture_names{1,i})= posture.Data;
clear posture
end
% emg_train_struct: 1x1 struct with 11 fields, each field (posture.Data) is a 8x167761 double
clear i;
% Raw EMG validation posture data
for i = 1:n_postures
load([posture_names{1,i},'_val.mat'])
emg_val_struct.(posture_names{1,i})= posture.Data;
clear posture
end
% emg_val_struct: 1x1 struct with 11 fields, each field (posture.Data) is a 8x167761 double
% EMG training data and validation data are equivalent in dimension -->
% save all data in a single storage container
%% Save each Raw EMG mat file struct (posture) in a single cell array
n_files = length(mat_files);
allData_cellArray = cell(cell(n_files, 2));
for i = 1:n_files
% 1st col: name of file struct (posture)
allData_cellArray{i, 1} = mat_files(i).name;
% 2nd col: content of file struct (posture)
allData_cellArray{i, 2} = load(mat_files(i).name);
end
clear i;
%% Plot all channels of Raw EMG per posture
n_channels = height(allData_cellArray{1,2}.posture.Channels);
for i = 1:length(allData_cellArray)
figure(i)
for j = 1:n_channels
subplot(4, 2, j);
plot(allData_cellArray{i,2}.posture.Time(j,:), allData_cellArray{i,2}.posture.Data(j,:));
title("Raw Data, Channel "+ j);
sgtitle(allData_cellArray{i,1}, 'Interpreter', 'none');
ylim([-2e-3, 2e-3]);
end
end

## Slide 4
Signal Processing – Filter Design
Details:
Input Data
Signal Processing Steps
  Filter Design w/ cutoff frequencies
    High pass: 30Hz to remove motion artefact - choose a multiple of 60Hz
    Low Pass: 480Hz to bandlimit to around 500Hz - choose a multiple of 60Hz
    Notch/Comb Filter: centered at 60Hz and its harmonics (120Hz, 180Hz, 240Hz, 300Hz, 360Hz, 420Hz) up to the passband (480 Hz); 2nd order infinite impulse response (IIR) notch filter
  “Off” section removal method
  Quiescent data removal method
Output Data
Notes: %% Filter Design plotting w/ cutoff frequencies
Fs = allData_cellArray{1, 2}.posture.Fs(1); % 2.2222e+03 Hz
% High Pass Filter - 30Hz to remove motion artefact - choose a multiple of 60Hz
[b_hp, a_hp] = butter(4, 30/(Fs/2), 'high'); % 4th order butterworth
% Low Pass Filter - 480Hz to bandlimit to around 500Hz - choose a multiple of 60Hz
[b_lp, a_lp] = butter(4, 480/(Fs/2), 'low'); % 4th order butterworth
% Notch Filter centered at 60Hz
f0 = 60; % Notch frequency
Q = 35; % Quality factor, q = ω0/bw where ω0 is the frequency to remove from the signal
[b_notch, a_notch] = iirnotch(f0/(Fs/2), f0/(Fs/2)/Q); % 2nd order infinite impulse response (IIR) notch filter
% Comb Filter centered at 60Hz and its harmonics (120Hz, 180Hz, 240Hz, 300Hz, 360Hz, 420Hz) up to the passband (480 Hz)
f0 = 60; % Notch frequency
bw = f0 / Q; % Bandwidth, bw = (fo/(fs/2))/q;
n_harmonics = floor((Fs / 2) / f0); % Number of harmonics within Nyquist frequency
[b_comb, a_comb] = iircomb(floor(Fs/f0), bw/(Fs/2), 'notch'); % Design comb filter
% Define quiescent threshold
quietThresh = mean(on_data(1,:)) + (0.5*std(on_data(1,:))); % Adjust multiplier as needed
% Initialize array to store 'active' data, where the muscle is not quiescent
active_data = [];
active_time = [];
% Define the bin size for iteration, could be the same as used for 'off' detection
binSize = 1.5e-3; % 1.5 ms in seconds
binSamples = round(binSize * Fs); % Convert bin size to number of samples
% Loop to identify and store 'active' data
for i = 1:binSamples:length(on_data(1,:)) - binSamples
segment = on_data(1, i:i+binSamples-1);
% Check if the segment's activity exceeds the quiescent threshold
if max(abs(segment)) > quietThresh
active_data = [active_data, segment];
active_time = [active_time, on_data_Time(1, i:i+binSamples-1)];
end
end
% Plot the 'active' data
figure;
plot(active_time, active_data, 'r-');
title('HO train, Sensor 1: EMG Data with Quiescent Data Removed');
xlabel('Time (s)');
ylabel('Amplitude');
ylim([-4e-4 4e-4]);
xlim([0, on_data_Time(1,end)]);
…
%% 4) Graph Mean Absolute Value, Slope Sign Change, Zero Crossings, Waveform Length value for the 50ms bin size and 2 EMG sensors in one posture ('HO_train.mat')
% Prepare the data for feature extraction
% Set the bin size to 50ms
binSize = 0.050; % 50 ms in seconds
binSamples = round(binSize * Fs); % Convert bin size to number of samples per bin
% Initialize feature matrices
MAV = cell(1, 2);
SSC = cell(1, 2);
ZC = cell(1, 2);
WL = cell(1, 2);
% Define active data for HO train, sensor 1 and sensor 2
active_data_s1s2 = {active_data, active_data_2};
% Loop over the 'active' data in bins to calculate features for each sensor
for sensor_idx = 1:2
active_data_sensor = active_data_s1s2{sensor_idx};
% Determine the number of full bins we can calculate
numBins = floor(length(active_data_sensor) / binSamples);
% Initialize the feature arrays for each sensor based on the number of bins
MAV{sensor_idx} = zeros(1, numBins);
SSC{sensor_idx} = zeros(1, numBins);
ZC{sensor_idx} = zeros(1, numBins);
WL{sensor_idx} = zeros(1, numBins);
for bin = 1:numBins
startIdx = (bin - 1) * binSamples + 1;
endIdx = bin * binSamples;
binData = active_data_sensor(startIdx:endIdx);
% Calculate features for each bin
MAV{sensor_idx}(bin) = mean(abs(binData));
SSC{sensor_idx}(bin) = sum(diff(sign(diff(binData)))~=0);
ZC{sensor_idx}(bin) = sum(diff(sign(binData))~=0);
WL{sensor_idx}(bin) = sum(abs(diff(binData)));
end
end
% Calculate feature_time based on the actual number of bins calculated
feature_time = ((1:numBins) - 0.5) * binSize; % Center time in each bin
% Verify the number of bins and adjust feature_time accordingly - test for single feature (MAV)
numBins = min([length(MAV{1}), length(MAV{2})]); % Use the smaller number of bins if different
feature_time = ((1:numBins) - 0.5) * binSize;
% Trim the feature vectors if necessary
MAV{1} = MAV{1}(1:numBins);
MAV{2} = MAV{2}(1:numBins);
% Debugging prints
disp(['Length of feature_time: ', num2str(length(feature_time))]);
disp(['Length of MAV{1}: ', num2str(length(MAV{1}))]);
disp(['Length of MAV{2}: ', num2str(length(MAV{2}))]);
% Now plot the features with the corrected lengths
figure;
title('Feature Extraction for HO_train');
% Plot Mean Absolute Value for Sensor 1 and Sensor 2
hold on;
plot(feature_time, MAV{1}, 'r');
plot(feature_time, MAV{2}, 'b');
title('Mean Absolute Value (MAV)');
xlabel('Time (s)');
ylabel('MAV');
legend('Sensor 1', 'Sensor 2');
hold off;
%% Verify the number of bins and adjust feature_time accordingly for all features
% Determine the smallest number of bins across all sensors and features
numBins = min([
length(MAV{1}), length(MAV{2}),
length(SSC{1}), length(SSC{2}),
length(ZC{1}), length(ZC{2}),
length(WL{1}), length(WL{2})
]);
% Adjust feature vectors to have the same number of elements
MAV{1} = MAV{1}(1:numBins);
MAV{2} = MAV{2}(1:numBins);
SSC{1} = SSC{1}(1:numBins);
SSC{2} = SSC{2}(1:numBins);
ZC{1} = ZC{1}(1:numBins);
ZC{2} = ZC{2}(1:numBins);
WL{1} = WL{1}(1:numBins);
WL{2} = WL{2}(1:numBins);
% Adjust feature_time
feature_time = ((1:numBins) - 0.5) * binSize;
%% Plot extracted features
figure;
t = tiledlayout(4,1);
title(t,'Feature Extraction for HO_train');
% Plot Mean Absolute Value
nexttile;
hold on;
plot(feature_time, MAV{1}, 'r', 'DisplayName', 'Sensor 1 MAV');
plot(feature_time, MAV{2}, 'b', 'DisplayName', 'Sensor 2 MAV');
title('Mean Absolute Value (MAV)');
xlabel('Time (s)');
ylabel('MAV');
legend;
hold off;
% Plot Slope Sign Changes
nexttile;
hold on;
plot(feature_time, SSC{1}, 'r', 'DisplayName', 'Sensor 1 SSC');
plot(feature_time, SSC{2}, 'b', 'DisplayName', 'Sensor 2 SSC');
title('Slope Sign Changes (SSC)');
xlabel('Time (s)');
ylabel('SSC');
legend;
hold off;
% Plot Zero Crossings
nexttile;
hold on;
plot(feature_time, ZC{1}, 'r', 'DisplayName', 'Sensor 1 ZC');
plot(feature_time, ZC{2}, 'b', 'DisplayName', 'Sensor 2 ZC');
title('Zero Crossings (ZC)');
xlabel('Time (s)');
ylabel('ZC');
legend;
hold off;
% Plot Waveform Length
nexttile;
hold on;
plot(feature_time, WL{1}, 'r', 'DisplayName', 'Sensor 1 WL');
plot(feature_time, WL{2}, 'b', 'DisplayName', 'Sensor 2 WL');
title('Waveform Length (WL)');
xlabel('Time (s)');
ylabel('WL');
legend;
hold off;

## Slide 5
Example Plots – Raw vs. Filtered Data
Raw data
Filtered Data
  Bonus:
    Freq. vs. Power plot of filtered data for single posture (e.g., pwelch plot)
    Filtered EMG data along time axis for each channel for a single posture, e.g., HO_train

## Slide 6
Signal Processing – “Off” & Quiescent Data Removal
Details:
Input Data
Signal Processing Steps
  Filter Design w/ cutoff frequencies
    High pass: 30Hz to remove motion artefact - choose a multiple of 60Hz
    Low Pass: 480Hz to bandlimit to around 500Hz - choose a multiple of 60Hz
    Notch/Comb Filter: centered at 60Hz and its harmonics (120Hz, 180Hz, 240Hz, 300Hz, 360Hz, 420Hz) up to the passband (480 Hz); 2nd order infinite impulse response (IIR) notch filter
  “Off” section removal method
  Quiescent data removal method
Output Data
Notes: %% Filter Design plotting w/ cutoff frequencies
Fs = allData_cellArray{1, 2}.posture.Fs(1); % 2.2222e+03 Hz
% High Pass Filter - 30Hz to remove motion artefact - choose a multiple of 60Hz
[b_hp, a_hp] = butter(4, 30/(Fs/2), 'high'); % 4th order butterworth
% Low Pass Filter - 480Hz to bandlimit to around 500Hz - choose a multiple of 60Hz
[b_lp, a_lp] = butter(4, 480/(Fs/2), 'low'); % 4th order butterworth
% Notch Filter centered at 60Hz
f0 = 60; % Notch frequency
Q = 35; % Quality factor, q = ω0/bw where ω0 is the frequency to remove from the signal
[b_notch, a_notch] = iirnotch(f0/(Fs/2), f0/(Fs/2)/Q); % 2nd order infinite impulse response (IIR) notch filter
% Comb Filter centered at 60Hz and its harmonics (120Hz, 180Hz, 240Hz, 300Hz, 360Hz, 420Hz) up to the passband (480 Hz)
f0 = 60; % Notch frequency
bw = f0 / Q; % Bandwidth, bw = (fo/(fs/2))/q;
n_harmonics = floor((Fs / 2) / f0); % Number of harmonics within Nyquist frequency
[b_comb, a_comb] = iircomb(floor(Fs/f0), bw/(Fs/2), 'notch'); % Design comb filter
% Define quiescent threshold
quietThresh = mean(on_data(1,:)) + (0.5*std(on_data(1,:))); % Adjust multiplier as needed
% Initialize array to store 'active' data, where the muscle is not quiescent
active_data = [];
active_time = [];
% Define the bin size for iteration, could be the same as used for 'off' detection
binSize = 1.5e-3; % 1.5 ms in seconds
binSamples = round(binSize * Fs); % Convert bin size to number of samples
% Loop to identify and store 'active' data
for i = 1:binSamples:length(on_data(1,:)) - binSamples
segment = on_data(1, i:i+binSamples-1);
% Check if the segment's activity exceeds the quiescent threshold
if max(abs(segment)) > quietThresh
active_data = [active_data, segment];
active_time = [active_time, on_data_Time(1, i:i+binSamples-1)];
end
end
% Plot the 'active' data
figure;
plot(active_time, active_data, 'r-');
title('HO train, Sensor 1: EMG Data with Quiescent Data Removed');
xlabel('Time (s)');
ylabel('Amplitude');
ylim([-4e-4 4e-4]);
xlim([0, on_data_Time(1,end)]);
…
%% 4) Graph Mean Absolute Value, Slope Sign Change, Zero Crossings, Waveform Length value for the 50ms bin size and 2 EMG sensors in one posture ('HO_train.mat')
% Prepare the data for feature extraction
% Set the bin size to 50ms
binSize = 0.050; % 50 ms in seconds
binSamples = round(binSize * Fs); % Convert bin size to number of samples per bin
% Initialize feature matrices
MAV = cell(1, 2);
SSC = cell(1, 2);
ZC = cell(1, 2);
WL = cell(1, 2);
% Define active data for HO train, sensor 1 and sensor 2
active_data_s1s2 = {active_data, active_data_2};
% Loop over the 'active' data in bins to calculate features for each sensor
for sensor_idx = 1:2
active_data_sensor = active_data_s1s2{sensor_idx};
% Determine the number of full bins we can calculate
numBins = floor(length(active_data_sensor) / binSamples);
% Initialize the feature arrays for each sensor based on the number of bins
MAV{sensor_idx} = zeros(1, numBins);
SSC{sensor_idx} = zeros(1, numBins);
ZC{sensor_idx} = zeros(1, numBins);
WL{sensor_idx} = zeros(1, numBins);
for bin = 1:numBins
startIdx = (bin - 1) * binSamples + 1;
endIdx = bin * binSamples;
binData = active_data_sensor(startIdx:endIdx);
% Calculate features for each bin
MAV{sensor_idx}(bin) = mean(abs(binData));
SSC{sensor_idx}(bin) = sum(diff(sign(diff(binData)))~=0);
ZC{sensor_idx}(bin) = sum(diff(sign(binData))~=0);
WL{sensor_idx}(bin) = sum(abs(diff(binData)));
end
end
% Calculate feature_time based on the actual number of bins calculated
feature_time = ((1:numBins) - 0.5) * binSize; % Center time in each bin
% Verify the number of bins and adjust feature_time accordingly - test for single feature (MAV)
numBins = min([length(MAV{1}), length(MAV{2})]); % Use the smaller number of bins if different
feature_time = ((1:numBins) - 0.5) * binSize;
% Trim the feature vectors if necessary
MAV{1} = MAV{1}(1:numBins);
MAV{2} = MAV{2}(1:numBins);
% Debugging prints
disp(['Length of feature_time: ', num2str(length(feature_time))]);
disp(['Length of MAV{1}: ', num2str(length(MAV{1}))]);
disp(['Length of MAV{2}: ', num2str(length(MAV{2}))]);
% Now plot the features with the corrected lengths
figure;
title('Feature Extraction for HO_train');
% Plot Mean Absolute Value for Sensor 1 and Sensor 2
hold on;
plot(feature_time, MAV{1}, 'r');
plot(feature_time, MAV{2}, 'b');
title('Mean Absolute Value (MAV)');
xlabel('Time (s)');
ylabel('MAV');
legend('Sensor 1', 'Sensor 2');
hold off;
%% Verify the number of bins and adjust feature_time accordingly for all features
% Determine the smallest number of bins across all sensors and features
numBins = min([
length(MAV{1}), length(MAV{2}),
length(SSC{1}), length(SSC{2}),
length(ZC{1}), length(ZC{2}),
length(WL{1}), length(WL{2})
]);
% Adjust feature vectors to have the same number of elements
MAV{1} = MAV{1}(1:numBins);
MAV{2} = MAV{2}(1:numBins);
SSC{1} = SSC{1}(1:numBins);
SSC{2} = SSC{2}(1:numBins);
ZC{1} = ZC{1}(1:numBins);
ZC{2} = ZC{2}(1:numBins);
WL{1} = WL{1}(1:numBins);
WL{2} = WL{2}(1:numBins);
% Adjust feature_time
feature_time = ((1:numBins) - 0.5) * binSize;
%% Plot extracted features
figure;
t = tiledlayout(4,1);
title(t,'Feature Extraction for HO_train');
% Plot Mean Absolute Value
nexttile;
hold on;
plot(feature_time, MAV{1}, 'r', 'DisplayName', 'Sensor 1 MAV');
plot(feature_time, MAV{2}, 'b', 'DisplayName', 'Sensor 2 MAV');
title('Mean Absolute Value (MAV)');
xlabel('Time (s)');
ylabel('MAV');
legend;
hold off;
% Plot Slope Sign Changes
nexttile;
hold on;
plot(feature_time, SSC{1}, 'r', 'DisplayName', 'Sensor 1 SSC');
plot(feature_time, SSC{2}, 'b', 'DisplayName', 'Sensor 2 SSC');
title('Slope Sign Changes (SSC)');
xlabel('Time (s)');
ylabel('SSC');
legend;
hold off;
% Plot Zero Crossings
nexttile;
hold on;
plot(feature_time, ZC{1}, 'r', 'DisplayName', 'Sensor 1 ZC');
plot(feature_time, ZC{2}, 'b', 'DisplayName', 'Sensor 2 ZC');
title('Zero Crossings (ZC)');
xlabel('Time (s)');
ylabel('ZC');
legend;
hold off;
% Plot Waveform Length
nexttile;
hold on;
plot(feature_time, WL{1}, 'r', 'DisplayName', 'Sensor 1 WL');
plot(feature_time, WL{2}, 'b', 'DisplayName', 'Sensor 2 WL');
title('Waveform Length (WL)');
xlabel('Time (s)');
ylabel('WL');
legend;
hold off;

## Slide 7
Example Plots – “On” Data (Off and Quiescent Data Removed)
Filtered Data with “Off” sections removed
Filtered data with quiescent data removed

## Slide 8
Feature Extraction Methods
Input Data
Feature Extraction
Mean Absolute Value (MAV) for each bin size (50ms, 100ms, 150ms, 200ms)
Slope Sign Change (SSC)
Zero Crossings (ZC)
Waveform Length (WL)
Output Data
Notes: %% 4) Graph Mean Absolute Value, Slope Sign Change, Zero Crossings, Waveform Length value for the 50ms bin size and 2 EMG sensors in one posture ('HO_train.mat')
% Prepare the data for feature extraction
% Set the bin size to 50ms
binSize = 0.050; % 50 ms in seconds
binSamples = round(binSize * Fs); % Convert bin size to number of samples per bin
% Initialize feature matrices
MAV = cell(1, 2);
SSC = cell(1, 2);
ZC = cell(1, 2);
WL = cell(1, 2);
% Define active data for HO train, sensor 1 and sensor 2
active_data_s1s2 = {active_data, active_data_2};
% Loop over the 'active' data in bins to calculate features for each sensor
for sensor_idx = 1:2
active_data_sensor = active_data_s1s2{sensor_idx};
% Determine the number of full bins we can calculate
numBins = floor(length(active_data_sensor) / binSamples);
% Initialize the feature arrays for each sensor based on the number of bins
MAV{sensor_idx} = zeros(1, numBins);
SSC{sensor_idx} = zeros(1, numBins);
ZC{sensor_idx} = zeros(1, numBins);
WL{sensor_idx} = zeros(1, numBins);
for bin = 1:numBins
startIdx = (bin - 1) * binSamples + 1;
endIdx = bin * binSamples;
binData = active_data_sensor(startIdx:endIdx);
% Calculate features for each bin
MAV{sensor_idx}(bin) = mean(abs(binData));
SSC{sensor_idx}(bin) = sum(diff(sign(diff(binData)))~=0);
ZC{sensor_idx}(bin) = sum(diff(sign(binData))~=0);
WL{sensor_idx}(bin) = sum(abs(diff(binData)));
end
end
% Calculate feature_time based on the actual number of bins calculated
feature_time = ((1:numBins) - 0.5) * binSize; % Center time in each bin
% Verify the number of bins and adjust feature_time accordingly - test for single feature (MAV)
numBins = min([length(MAV{1}), length(MAV{2})]); % Use the smaller number of bins if different
feature_time = ((1:numBins) - 0.5) * binSize;
% Trim the feature vectors if necessary
MAV{1} = MAV{1}(1:numBins);
MAV{2} = MAV{2}(1:numBins);
% Debugging prints
disp(['Length of feature_time: ', num2str(length(feature_time))]);
disp(['Length of MAV{1}: ', num2str(length(MAV{1}))]);
disp(['Length of MAV{2}: ', num2str(length(MAV{2}))]);
% Now plot the features with the corrected lengths
figure;
title('Feature Extraction for HO_train');
% Plot Mean Absolute Value for Sensor 1 and Sensor 2
hold on;
plot(feature_time, MAV{1}, 'r');
plot(feature_time, MAV{2}, 'b');
title('Mean Absolute Value (MAV)');
xlabel('Time (s)');
ylabel('MAV');
legend('Sensor 1', 'Sensor 2');
hold off;
%% Verify the number of bins and adjust feature_time accordingly for all features
% Determine the smallest number of bins across all sensors and features
numBins = min([
length(MAV{1}), length(MAV{2}),
length(SSC{1}), length(SSC{2}),
length(ZC{1}), length(ZC{2}),
length(WL{1}), length(WL{2})
]);
% Adjust feature vectors to have the same number of elements
MAV{1} = MAV{1}(1:numBins);
MAV{2} = MAV{2}(1:numBins);
SSC{1} = SSC{1}(1:numBins);
SSC{2} = SSC{2}(1:numBins);
ZC{1} = ZC{1}(1:numBins);
ZC{2} = ZC{2}(1:numBins);
WL{1} = WL{1}(1:numBins);
WL{2} = WL{2}(1:numBins);
% Adjust feature_time
feature_time = ((1:numBins) - 0.5) * binSize;
%% Plot extracted features
figure;
t = tiledlayout(4,1);
title(t,'Feature Extraction for HO_train');
% Plot Mean Absolute Value
nexttile;
hold on;
plot(feature_time, MAV{1}, 'r', 'DisplayName', 'Sensor 1 MAV');
plot(feature_time, MAV{2}, 'b', 'DisplayName', 'Sensor 2 MAV');
title('Mean Absolute Value (MAV)');
xlabel('Time (s)');
ylabel('MAV');
legend;
hold off;
% Plot Slope Sign Changes
nexttile;
hold on;
plot(feature_time, SSC{1}, 'r', 'DisplayName', 'Sensor 1 SSC');
plot(feature_time, SSC{2}, 'b', 'DisplayName', 'Sensor 2 SSC');
title('Slope Sign Changes (SSC)');
xlabel('Time (s)');
ylabel('SSC');
legend;
hold off;
% Plot Zero Crossings
nexttile;
hold on;
plot(feature_time, ZC{1}, 'r', 'DisplayName', 'Sensor 1 ZC');
plot(feature_time, ZC{2}, 'b', 'DisplayName', 'Sensor 2 ZC');
title('Zero Crossings (ZC)');
xlabel('Time (s)');
ylabel('ZC');
legend;
hold off;
% Plot Waveform Length
nexttile;
hold on;
plot(feature_time, WL{1}, 'r', 'DisplayName', 'Sensor 1 WL');
plot(feature_time, WL{2}, 'b', 'DisplayName', 'Sensor 2 WL');
title('Waveform Length (WL)');
xlabel('Time (s)');
ylabel('WL');
legend;
hold off;

## Slide 9
Example Plots
Graph of Mean Absolute Value for each bin size (50ms, 100ms, 150ms, 200ms) for 1 EMG sensor in one posture
Graph of Mean Absolute Value, Slope Sign Change, Zero Crossings, Waveform Length value for 50ms bin size and 2 EMG sensors, one posture

## Slide 10
Mean Vectors
Mean vectors (one slide)
? Functions and reasoning

## Slide 11
Scatter Matrices
Scatter Matrices (Sb,Sw, O) separate slides
posture feautrure matrices (train)
8 EMGs, 4 feaures
32 x 32 matrix - covariance matrix (of feautures)
add up, devide by numPostures
within-class scatter matrix
diag = standard dev.
? Functions and reasoning

## Slide 12
Eigenvectors & Eigenvalues
Print eigenvectors and values
10 eigenvals
10 eigenvecs
? Functions, math, and reasoning

## Slide 13
Transformation (W) Matrix
Print W matrix
W matrix will be 32 x n (transformation matrix: control)
n=10
? Functions, math, and reasoning
Classification strategy

## Slide 14
Confusion Matrix
Print Confusion matrix; Explain results
W matrix will be 32 x n (transformation matrix: control)
n=10
? Functions, math, and reasoning

## Slide 15
Discussion
From Canvas:
Take-aways
What bin sizes did you use, why?
What coding issues did you have handling large data sets?
What can you say about the identification and removal of the quiescent data? Relevance?
How you would improve your process if you had more time?
Advice for the next class regarding this assignment.

## Slide 16
Neural Interfaces and Bionic Limbs Spring 2024
Thank you! | Questions?
Timothy Young, Erin Radcliffe, Sari Younan, Fai Au
GitHub Project Repo:https://github.com/sayounan/RoboArms

## Slide 17
Final Project: LDA Code (from Canvas)
  Please submit your group's code here as a HTML zip file or pdf.
  Must be able to read graphs and subplots for each channel.
Code should include:
  Raw time domain data plots
  Sampling frequency
  Filter plots (high pass, lowpass, bandpass, or notch)
  Frequency spectrum of raw and filtered data.
  Filtered time domain data plots
  Feature plots (MAV, ZC, SSC, WL) with bin size specified
  Off removal plots
  Sections of LDA code (Cov matrix, Sw, Sb, O, W, eig, Y, dist, Confusion Matrix)
EMG data collection setup pictures and subject information should also be included in a separate zip file.
Please note: commenting code and adding brief explanations help us figure out what's going on when grading!